## Slide 1
Couch & Couch motor
1D platform
RealSense depth camera
a)
b)

## Slide 2: Couch Tracking Flowchart –with Intel Realsense depth camera UDPsender_realtime.py
Couch
Input Trace
Couch Motor
Depth camera
Frame No. Timestamp, ROI1, ROI2
Platform moves in 1D, based on the input trace.
Depth camera measures depth values in real-time. Write to csv file, frame number, timestamp, ROI1 depth values (1D platform), ROI2 depth values (couch)
Couch is receiving ROI1 depth values via UDP in real-time. Motor travel in opposite direction of 1D platform to achieve motion compensation.
*** For code details please see couch tracking pseudocode document.
1D platform

## Slide 3: Couch Tracking with pre-recorded trace Flowchart – UDPsend_trace.py
Input Trace
Depth camera
Frame No. Timestamp, ROI1, ROI2
UDP sender
Couch Motor
Depth camera
Frame No. Timestamp, ROI1, ROI2
1D platform
Couch

## Slide 4
6 degree-of-freedom Robotic arm
Couch
Motor
Intel Realsense depth camera

## Slide 5
Tracking Target
(6Dof Robotic arm/
1D motion platform)
Movable Couch
Tracking Tool
(KIM/
Depth measurement)
Target being tracked,
Positional measurement generated
Measurements are sent to couch via UDP

## Slide 6: Couch Hardware
Couch Motor
https://www.firgelliauto.com.au/products/bullet-series-50-cal-linear-actuators
Tested highest speed 12mm/s with no load. Higher load decreases the motor speed.
System control
Raspberry Pi enables motor operation and executes motion compensation.
Raspberry Pi Model 4B 8GB RAM with at least 16GB SD card.
https://www.raspberrypi.com/products/raspberry-pi-4-model-b/